THE EKSTRA LOUDSPEAKER

INSTRUCTIONS FOR USE

Congratulations on choosing the Neat Ekstra loudspeakers. Used correctly, they will provide a lifetime of beautiful music. Please read the following notes in order to get the best from them.

RUNNING IN

A 'running in' period of at least 200 hours is necessary to stabilise performance. After this period, a further gradual improvement will occur over a period of several weeks.

FIRST

1) Unpack and place loudspeaker upside-down in one of the foam packing inserts.

2) Take the aluminium feet (3 per cabinet) from the internal packing box and fit them to the bottom panel of the speaker using the supplied M6 fixing screws and the 4mm allen key.

(The feet should be located one at each side towards the front of the cabinet, and one at the rear of the cabinet).

NB: Place a washer on the screws between the aluminium foot and the bottom of the cabinet, as shown;

2) Place a locking ring on each spike, with the narrow end of the locking ring towards the spike end. Fit the spikes to the threaded inserts on each foot.

4) Return the speaker to upright and place in the appropriate listening position (see "Positioning" below).

5) Level by adjusting the spikes, and tighten locking rings firmly by hand.

CONNECTION

The Ekstra can accept 4mm banana plugs, spade connectors or bare wire. Ensure a tight fit for banana plugs. For bare wire or spade connections, ensure that the binding post outer part is screwed down tight.

Take care to ensure correct phasing (i.e. red and black connections maintained at amplifier and speaker).

POSITIONING

Important note: Best listening results will be obtained without the grilles!

The Ekstra is intended for close to wall placement. Due to huge variations in the acoustic properties of different rooms, there are few hard and fast rules governing loudspeaker positioning so experimentation is recommended. Generally, bass output increases as distance from the rear wall, or side wall, decreases. Stereo depth improves as the speaker is brought away from room boundaries. Start with the rear of the speaker at approx. 20cm from the rear walls, and 50cm from side walls. Make incremental moves in different directions, noting the changes, until an optimal position is reached. Remember that sometimes very small movements of the loudspeaker can bring about huge differences in performance.

MAINTENANCE

The EKSTRA has no user-replaceable parts and requires no maintenance.

To clean the cabinet, brush lightly with a dry sponge. The bass/midrange cone can be cleaned by GENTLY using a soft, very lightly damp cloth. Do not touch the tweeter diaphragm. Should a fault condition arise, consult your dealer.

WARRANTY

The Ekstra is guaranteed against defects in materials and workmanship for a period of five years.

SPECIFICATIONS

| ENCLOSURE TYPE | 2.5-way bass reflex, with iso-baric bass section. |
| --- | --- |
| DIMENSIONS | 1100/170/270mm (HxWxD). |
| FEET FOOTPRINT | 270 X 320 mm. (WxD) |
| WEIGHT | 20 Kg. each. (SHIPPING WEIGHT: 46kg. pr.) |
| SENSITIVITY (2.83v/1m) | 86 dB/1 watt. |
| RECOMMENDED AMPLIFIER POWER | 25 to 150 watts. |
| IMPEDANCE | 6 Ohms |

(Specification may be subject to change without notice)

Neat Acoustics Ltd., 29 Harmire Enterprise Park, Co. Durham, DL12 8XT, U.K.

Tel: + 44 1833 631021  www.neatacoustics.com